## Slide 1: Master Thesis: RSS-based localization using distributed spectrum sensing for 5G networks
Lehrstuhl Elektrische Smart City Systeme
Nuremberg Campus of Technology (NCT)
Prof. Dr.-Ing. Norman Franchi
Engineering for Smart Cities
Begin: 1.04. 23
End: 2.10.23
Supervisors:
Victor Shatov
Norman Franchi
Student:
Aakarsh Dhariwal
19.10.2023

## Slide 2: Outline
Introduction
2
Methodology
3
REM construction
4
Conclusion
5
References
6
Motivation and objective
1
4
5

## Slide 3: Motivation and objective
Localization of active transmitter supports many location based services and applications such as security, spectrum occupancy.
Received signal strength (RSS) measurements captured from sensors as a means to perform localization.
Using the estimated position to estimate power map or radio environment map (REM) of the transmitter.
In a certain area

## Slide 4: Motivation and objective
Figure 1: Applications of localization [2], [4].
Some explaining text on the right?
Slide look too empty
Fit under the line when there’s
enough space

## Slide 5: RSS as a suitable technology for localization
Figure 2: Motivation for using RSS measurements for localization [6].

## Slide 6: Introduction and Proposed scenario [1],[2]
Figure 3: Scenario for localization using dedicated sensor network [1], [2] and REM construction.
Some text +
to make the figure smaller?
Would also mask
rather poor resolution...

## Slide 7: REM Data Model
Figure 4 : REM architecture [4].
Is it just the architecture, or smth more?..

## Slide 8: Goals of the thesis
Comparing and evaluating the localization accuracy of MSE and LIvE methods.
Assuming OFDM signal as a transmit signal and evaluating performance of MSE method.
Assuming correlated shadowing and evaluating the localization error using varying standard deviation of shadowing.
Constructing estimated and true REM using results of localization from MSE-based method.
REM as a emerging tool for 5G use cases such as ultra low latency, mobility, dynamic changes in channel.

## Slide 9: Methodology and overall process
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 5: Methodology flow diagram.
No output further from the fusion center to the signal processing chain?
Maybe use more colors to make it look prettier?

## Slide 10: Dedicated sensor network
Sensor arrangement
9. Oktober 2023
8
Figure 6: Placement of dedicated sensor network 4,9,25 and sensors with true transmitter position [18 m, 37 m] in a grid of [100 m, 100 m] [1].
Figures are visibly stretched
horisontally

## Slide 11: Methodology and overall process
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 7:System model and parameters modeling.
If there’s nothing except for figure,
maybe better to place it in the center?
space

## Slide 12: System Model
Considering a simple path loss model the RSS measurement at j-th node is given as [2]:
(1)
path loss exponent.
: reference distance
PL_0: reference path loss
: transmit power
Shadowing
PL0
Why do you introduce variables
above and below the equation?...

## Slide 13: System Model [1],[2]
Considering a simple path loss model the RSS measurement at j-th node is given as [2]:
(1)
d in the equation (1) is given by:
(2)
path loss exponent..
: reference distance.
reference path loss.
: transmit power.
Shadowing
The same comment from previous slide

## Slide 14: System model parameters
Sensor arrangement
System model and parameter settings
path loss exponent 3.5 [1].
: reference distance 2 m.
: 0.1 Watts [1].
(shadowing variance) 8 dB [1].
Frequency: 3.7 GHz [6].
True transmitter position [18 m, 37 m].
Number of experiments for averaging 25.

## Slide 15: Methodology and overall process
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 8: RSS measurements calculation.

## Slide 16: Collection of RSS measurements
Figure 9: Calculating RSS measurements and performing localization [5].

## Slide 17: MSE method for localization
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Performance Evaluation
REM construction
Figure 10: Methodology and flow diagram.

## Slide 18: MSE-based localization[1]
Problem formulation
(3)
𝐴𝜃=𝑏 (3)
MSE solution
(4)
〖 𝜃〗_𝑜𝑝𝑡= ((∑𝐴_𝑖^𝑇 𝑏_𝑖)/(∑𝐴_𝑖^𝑇 𝐴_𝑖 )) (4)
RESULT
combinations of sensors.
〖𝐶^𝑁〗_4 combinations of sensors.
Perform the operations for 25 experiments to average the result
A: input parameter matrix
unknown parameter
𝜃: unknown parameter
b: output parameter vector
MSE solution
RESULT

## Slide 19: Simulation result
Figure 11: Localization error for MSE method.
Figure 12: Localization error against increasing grid size.

## Slide 20: LIvE method for localization
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 13: Methodology and flow diagram.

## Slide 21: LIvE-based localization[3]
Problem formulation:
𝐴𝜃=𝑏
LIvE solution
(5)
𝐿(𝜃,𝜆) = 〖(𝐴 𝜃−𝑏)〗^𝑇 (𝐴 𝜃−𝑏) + 𝜆(𝑟^𝑇 𝜃+ 𝜃^𝑇 𝑃𝜃) (5)
RESULT
Perform the operations for 25 experiments to average the result
A: input parameter matrix
unknown parameter
𝜃: unknown parameter
b: output parameter vector
LIvE solution
RESULT
Perform the operations for 25 experiments to average the result
(5)

## Slide 22: Simulation result
Figure 14: Localization error for LIvE method.

## Slide 23: Localization accuracy evaluation
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 15: Localization accuracy evaluation of the MSE and LIvE methods.

## Slide 24: Performance Evaluation
Limitations
Infeasible point problem with optimization constraints in LIvE.
Tadeoff between better localization accuracy and complexity in solving non-linear constraints.
So for ease of implementation in real time we accept such tradeoff and use MSE for REM construction.
Figure 16: Localization accuracy evaluation of the MSE and LIvE methods

## Slide 25: Extension of system model: OFDM transmit signal
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 17: Employing use of OFDM as a transmit signal for localization.

## Slide 26: OFDM waveform generation and system parameters
28 OFDM symbols.
FFT size: 128 samples.
Cyclic prefix length 16.
Frequency 3.7 GHz [4].
2 subframes from numerology 0.
Figure 18: Generated OFDM waveform.

## Slide 27: Simulation result
Figure 19: Localization accuracy for OFDM signal using MSE method.

## Slide 28: Extension of system model: Correlated shadowing
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 20: Employing use of OFDM as a transmit signal for localization.

## Slide 29: Extension of system model: Correlated shadowing
Gudmundson model for correlated shadowing is given by the equation [9]:
(6)
System parameters used:
                Standard deviation : [0,4,8] dB.
                Correlation distance : 8 m [7].
covariance matrix
Distance between the sensors

## Slide 30: Simulation results
Figure 21: Localization error using MSE method with standard deviation of shadowing [0,4,8] dB.

## Slide 31: REM construction
Sensor arrangement
System model and parameter settings
RSS measurements calculations
OFDM transmit signal
Correlated shadowing
RSS-based localization
Fusion center
MSE method
LIvE method
Evaluation
REM construction
Figure 22: Localization accuracy evaluation of the MSE and LIvE methods.

## Slide 32: REM construction
Figure 23: REM construction using active transmitter estimated and true location [1].
(Some) explanatory text would fit good
And the fig. resolution is rather low...

## Slide 33: REM flow diagram
Figure 24: REM data flow and model [4].
Finally a very nice and neat figure 

## Slide 34: True and estimated power maps
Figure 25: True and estimated REM using the estimated location from MSE method in a grid of size (100 m, 100m).

## Slide 35: True and estimated power maps
With additive log-normal shadowing
Figure 26: True and estimated REM using the estimated location from MSE method in a grid of size (100 m, 100m).

## Slide 36: REM applications
Figure 27: REM applications and use cases [8].

## Slide 37: Main contributions
Comparing and evaluating the localization accuracy of MSE and LIvE methods.
Assuming OFDM signal as a transmit signal and evaluating performance of MSE method.
Assuming correlated shadowing and evaluating the localization error using varying standard deviation of shadowing.
Constructing estimated and true REM using results of localization from MSE-based method.
REM as a emerging tool for 5G use cases such as ultra low latency, mobility, dynamic changes in channel.

## Slide 38: Conclusion
Evaluating MSE and LIvE methods we don’t see much convergence in terms of localization error from 25 sensor nodes while the convergence.
Using OFDM as a transmit signal for localization converges close to true transmitter position after 9 sensor nodes leaving the use of more sensor nodes redundant.
Shadowing correlations between the sensor nodes leads to increase in localization error as the shadowing standard deviation increases which increases correlations between the sensor nodes.
We choose MSE over LIvE method in terms of complexity in solving non-linear constraints and higher simulation run time.
Using results of MSE method for localization we get as close to true REM.

## Slide 39: Future Work
Effect of multipath fading, change of sensor placement and channel models to get more out of localization methods.
Finding an algorithm that also suffices mobility of transmitter and accuracy to the resolution of 0.1 m for V2X and autonomous driving cases.
Detailed analysis of OFDM waveform’s performance in terms of localization accuracy varying parameters and channel models.
Mobile scenarios instead of static scenario to evaluate localization and REM construction.

## Slide 40: References
Ezzati, Nematollah, Hasan Taheri, and Tuna Tugcu. "Optimised sensor network for transmitter localisation and radio environment mapping." IET Communications 10.16 (2016): 2170-2178. Location estimation-based radio environment map construction in fading channels.
Yilmaz, Huseyin Birkan, and Tuna Tugcu. "Location estimation‐based radio environment map construction in fading channels." Wireless communications and mobile computing 15.3 (2015): 561-570.
Yilmaz, H. Birkan, et al. "Radio environment map as enabler for practical cognitive radio networks." IEEE Communications Magazine 51.12 (2013): 162-169.
Phillips, Caleb, et al. "Practical radio environment mapping with geostatistics." 2012 IEEE International Symposium on Dynamic Spectrum Access Networks. IEEE, 2012.
Reddy, Yeduri Sreenivasa, et al. "Spectrum cartography techniques, challenges, opportunities, and applications: A survey." Pervasive and Mobile Computing 79 (2022): 101511.

## Slide 41: References
Reddy, Yeduri Sreenivasa, et al. "Spectrum cartography techniques, challenges, opportunities, and applications: A survey." Pervasive and Mobile Computing 79 (2022): 101511.
De Almeida, Ivo Bizon Franco, et al. "Blind transmitter localization in wireless sensor networks: A deep learning approach." 2021 IEEE 32nd Annual International Symposium on Personal, Indoor and Mobile Radio Communications (PIMRC). IEEE, 2021.
Turkmen, H., Solaija, M. S. J., Furqan, H. M., & Arslan, H. (2020). Generalized Radio Environment Monitoring for Next Generation Wireless Networks. arXiv preprint arXiv:2008.06203.
Kulkarni, K., Franchi, N., & Fettweis, G. (2019, February). Real-time cooperative spectrum sensing: Reliable localization of unknown interferers in shared spectrum. In SCC 2019; 12th International ITG Conference on Systems, Communications and Coding (pp. 1-6). VDE.

## Slide 42: Applications of REM Construction
Figure 3 : REM applications use cases [5]

## Slide 43: RSS Based Transmitter Localization Model
The received power levels at the sensor nodes in a network are the input measurements.
The operation network area where we perform Tx localization consists of several important characteristics of radio environment.
The characteristics to model RF area are:
          Propagation channel model (Path Loss model),.
          Positioning of Tx and sensor nodes.
          Frequency of transmission.
          Small Scale or Large Scale fading, static or mobile scenario.
          Number of active Transmitters and Sensors deployed.

## Slide 44: System Model
The arrangement of sensor nodes in the previous figure are lying in an operation area where we collect the RSS values.
RSS values depend on the propagation environment, and spatial arrangement of the sensors.
We consider the simplistic path loss model with shadowing for channel analysis.
The network consists of static transceivers as point sources that operate in single channel and frequency in operation.
We consider a single frequency channel to avoid interference [2].

## Slide 45: System Model
Considering a simple path loss model the RSS measurement at j-th node is given as:
(1)
where, d is the euclidean distance between the j-th node and Tx located at positions. is the reference distance and is the log-normal shadowing (Gaussian distributed) noise with zero mean and variance.
And, , and are the received power at the j-th node, transmitter power and the path loss exponent respectively.
d in the equation (1) is given by:
(2)

## Slide 46: System Model: Adaptive Iterative and MSE Based Methods
Replacing d and after some manipulations of the received power formulation, we get:
(3)
The linear regression equation is given as:
(4)
The input parameter matrix (A), squared sensor coordinates vector b and parameter consisting Tx positions and Tx power is vector .
4 sensors measurements are used to perform localization.

## Slide 47: System Model: Adaptive Iterative and MSE Based Methods
The equation to calculate the unknown Tx positions for Adaptive Iterative in the parameter is given by:
(6)
Where is the step size.
is the instantaneous error.
The solution to estimate the Tx positions using MSE based method is given by:
(7)

## Slide 48: System Model: LIvE Method
  The optimal solution for LIvE is given as:
  (8)
The constrained optimization problem is solved using the dual Lagrange problem:
(9)

## Slide 49: Appendix 1
The linear regression equations for Tx localization algorithms are mentioned here.
A is the input parameter matrix, is the parameter vector to be estimated which consists of Tx coordinates and extra power term, b is the vector consisting of coordinates squared.
; ;
Which becomes of the form .

## Slide 50: Appendix 2
The linear regression equations for Tx localization algorithms are mentioned here.
A is the input parameter matrix, is the parameter vector to be estimated which consists of Tx coordinates and extra power term, b is the vector consisting of coordinates squared.
b